## Slide 1: Introduction to image analysis
April 2018
Adam Tyson

## Slide 2
Aims
Introduction to fundamental image analysis principles
Using ImageJ/FIJI (but everything is general)
Convert biological question into computational problem
Some parts will be very simple. Some parts won’t.
The aim is to help you understand image analysis for your PhD/postdoc/career, not to be able to use ImageJ by the end of the day.
Like anything, requires practice.
Disclaimer:
Email me whenever – adam.tyson@icr.ac.uk

## Slide 3
Questions
Are you currently using microscopy or planning to?
Which system(s)?
  Confocal/spinning disk
  Multiphoton
  High content (Celigo/Operetta/ImageXpress)
  TIRF
  Lightsheet
  Any others?
Which analysis software?
A bit / no / lots of experience?
Any specific aims?

## Slide 4
First (and most important lesson)
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 5
Software
Notes: Lots of software. Not much point teaching a specific one, going to go through fundamental principles.

## Slide 6
FIJI (FIJI is just ImageJ)
Free
Open source
Cross platform
Flexible
Huge community
http://forum.imagej.net/
https://fiji.sc/

## Slide 7
Why computational image analysis?
Quantity of data (TB’s per day)
Reproducibility, comparison
Notes: Lots of data, can’t analyse manually. Inspection of data doesn’t help when comparing lots of studies.

## Slide 8
Why computational image analysis?
Visual system relies heavily on context and relative changes.
Checker shadow illusion, Edward Adelson 1995.
Jastrow illusion, Joseph Jastrow (and others), 1892.
Notes: Most importantly – eye is very easy to fool.

## Slide 9
Nearly all microscopy images aren’t colour

## Slide 10
Lookup tables (LUTs)

## Slide 11
Images are arrays of numbers
78 | 64 | 71 | 57 | 43 | 44
86 | 93 | 69 | 60 | 48 | 46
75 | 64 | 57 | 59 | 55 | 62
70 | 65 | 69 | 85 | 56 | 54
54 | 68 | 88 | 63 | 46 | 43
51 | 51 | 74 | 66 | 43 | 35
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 12
More complicated images are still arrays of numbers
2D
78 | 64 | 71 | 57 | 43 | 44
86 | 93 | 69 | 60 | 48 | 46
75 | 64 | 57 | 59 | 55 | 62
70 | 65 | 69 | 85 | 56 | 54
54 | 68 | 88 | 63 | 46 | 43
51 | 51 | 74 | 66 | 43 | 35
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 13
More complicated images are still arrays of numbers
2D
Time-lapse
3D
3D time-lapse
RGB
3D RGB
3D RGB time-lapse
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 14
Image processing vs analysis
Volume
Shape
Texture
Notes: During image analysis, lots of the work will be image processing, i.e. getting the image ready to be analysed.

## Slide 15
Histogram
Open any sample image
Open histogram
Notes: Histogram shows how many pixels are of each possible intensity,

## Slide 16
Thresholding
Threshold (κ)
Notes: To perform a simple threshold, pick a point on the histogram. All pixels below a point belong to one class, and all pixels above it belong to the other.

## Slide 17
Thresholding
Notes: Choosing the right value for this threshold is obviously important. Too high, and features of interest won’t be detected. Too low, and other structures in the image will be detected too.

## Slide 18
Thresholding – try it out
Open DAPI.tif
Threshold

## Slide 19
Manual threshold - problems
DAPI.tif
DAPI_2.tif

## Slide 20
Automatic thresholding – Equal masses
Real case
Ideal case

## Slide 21
Automatic thresholding – Otsu’s method
Minimise within class variance (σW)
Maximise between class variance (σB)
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 22
Unimodal thresholding – Rosin’s method
Rosin (2001) Pattern Recognition. Vol 34, No 11, p2083
Use shape of distribution to find threshold

## Slide 23
Try it out – Otsu’s method
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 24
Many, many other methods
Kapur et al. (1985) Graphical Models and Image Processing Vol 29, No 3, p273

## Slide 25
Not always that simple …
Open DAPI_3.tif
Pick a threshold
vs

## Slide 26
Background subtraction – e.g. vignetting
Sample
Microscope
Image

## Slide 27
Background subtraction – e.g. vignetting
How to calculate??

## Slide 28
Estimate background – Gaussian smoothing
Seems arbitrary, but smoothing is often a key step in image processing
Try a value of 200 pixels

## Slide 29
Estimate background – Gaussian smoothing
May need to adjust brightness

## Slide 30
Estimate background

## Slide 31
Now try thresholding
Better, but not great

## Slide 32
Morphological operations
Processing of (usually binary) images based on shape

## Slide 33
Morphological operations
Try on the previous example
Eroded
Thresholded
Dilated and closed

## Slide 34
Watershed – separate objects
From the previous example
Notes: Basic implementation in ImageJ – but often requires a lot of tweaking if you don’t have two perfectly circular objects.

## Slide 35
Watershed
Distance transform
Negative intensity profile
Watershed

## Slide 36
Filters - Gaussian
Large kernel (200 pix)
Correct inhomogeneous illumination

## Slide 37
Filters - Gaussian
Smooth intensity variations for thresholding
Small kernel (8 pix)

## Slide 38
Filters - Gaussian
Open foci.tif & try thresholding
Apply Gaussian smoothing (use preview) & try again
vs

## Slide 39
Filters - Gradient
Edge detection
Approximate derivative:
  The Sobel operator
*
*

## Slide 40
Filters - Gradient

## Slide 41
Filters - Gradient
Combine

## Slide 42
Boolean image mathematics
AND
OR
XOR

## Slide 43
Boolean image mathematics - masking
PV.tif
PV_DAPI.tif
PV_seg.tif

## Slide 44
First (and most important lesson) – again!
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 45
Deconvolution
Sample
Blurred
Blurred & noisy
PSF
Noise
?

## Slide 46
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Deconvolved
Estimate
Compare with raw
Improve estimate
Convolved
estimate
PSF
Raw Image
Image
Operation

## Slide 47
Deconvolution – try it out
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
DeconvolutionLab2 (already installed)
Drag and drop
CElegans-FITC.tif
PSF-CElegans-FITC.tif
C. Elegans embryo - microtubules
Sage et al. (2017) Methods. Vol 115, p28

## Slide 48
Deconvolution – try it out (hopefully)
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
Deconvolution is computationally intense – may be very slow on these machines
Try “Regularized Inverse Filter”
Richardson-Lucy – start with 10 iterations - compare

## Slide 49
Deconvolution – notes
Not always necessary
Only an estimate of fluorophore distribution
100’s of algorithms and options – try them out
Can be very slow
Requires a good quality measured PSF (estimated PSF’s can work for standard microscopes)
  Routine to measure each day on light-sheet systems (e.g. lattice)
GIGA – Garbage In, Garbage Out

## Slide 50
Machine Learning
Often intensity alone can’t be used for segmentation
Need “context”
Train the computer to “recognize” structures
Open CHO.tif

## Slide 51
Machine Learning
Try to threshold!

## Slide 52
Machine Learning – Trainable Weka Segmentation

## Slide 53
Machine Learning – Trainable Weka Segmentation

## Slide 54
Machine Learning – Trainable Weka Segmentation
Lots of training data
Choose features carefully
iLastik
Will be slow!

## Slide 55
Analysis (rather than processing)
Measure segmented objects

## Slide 56
Analysis
Measure other objects
  Draw, then measure

## Slide 57
Analysis
Multiple objects – ROI manager

## Slide 58
Analysis – 3D

## Slide 59
Macros - record
Automated
Quicker
Reproducible (sharing)
Less chance for bias/mistakes
Works with most ImageJ plugins
No coding required (but possible)

## Slide 60
Macros – edit & run
Use comments (lines starting with “//”) for notes/explanations

## Slide 61
How to make your analysis easier – plan!
Use the correct method
  Widefield
  Confocal
  Multiphoton
  TIRF
  Super resolution (PALM/STORM/SRRF)
  Light sheet (iSPIM/diSPIM/Lattice)
  Something else – flow cytometry, biochemistry?
Choose dyes carefully (SNR!)
  mNeonGreen vs EGFP
  Alexa 488 vs FITC

## Slide 62
Resolution
Resolution depends on:
  Wavelength of light
  Refractive index of media (n)
  NA of objective
  (Width of light sheet)
Nyquist theorem
  Sampling frequency (how many pixels) should be ≤ resolution
  Modern acquisition software will do this for you.

## Slide 63
Resolution – However!
What do you want to image?
0.916 pix μm-1
15.4 pix μm-1
Same information – 300 x less data
  Also maybe quicker and more gentle

## Slide 64
Resolution – 3D
If you want to analyse in 3D:
  Isotropic resolution
2D
3D

## Slide 65
Note – 3D analysis
Analysis almost always exactly the same as 2D:
  Takes longer
  Need to view in 3D to check
  3D not necessarily supported by software package

## Slide 66
Resolution – temporal

## Slide 67
Resolution – temporal
Accurate sampling vs photobleaching & data size

## Slide 68
Signal to noise ratio (SNR)
Resolution irrelevant if you can’t detect structures of interest
High resolution
Low resolution
High SNR
Low SNR
Contrast often the most important aspect of a good image

## Slide 69
Analysis as a method
“True” image
Observed widefield image

## Slide 70
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 71
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
Localised fluorophores
Reconstructed image
STORM/PALM

## Slide 72
First (and most important lesson) – again!
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 73
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution
Tracking
Writing custom scripts – MATLAB / Python etc
Anything else?

## Slide 74: Introduction to image analysis
April 2018
Adam Tyson

## Slide 75
Aims
Introduction to fundamental image analysis principles
Using ImageJ/FIJI (but everything is general)
Convert biological question into computational problem

## Slide 76
Aims
Introduction to fundamental image analysis principles
Using ImageJ/FIJI (but everything is general)
Convert biological question into computational problem
Some parts will be very simple. Some parts won’t.
The aim is to help you understand image analysis for your PhD/postdoc/career, not to be able to use ImageJ by the end of the day.
Like anything, requires practice.
Disclaimer:

## Slide 77
Aims
Introduction to fundamental image analysis principles
Using ImageJ/FIJI (but everything is general)
Convert biological question into computational problem
Some parts will be very simple. Some parts won’t.
The aim is to help you understand image analysis for your PhD/postdoc/career, not to be able to use ImageJ by the end of the day.
Like anything, requires practice.
Disclaimer:
Email me whenever – adam.tyson@icr.ac.uk

## Slide 78
Questions

## Slide 79
Questions
Are you currently using microscopy or planning to?

## Slide 80
Questions
Are you currently using microscopy or planning to?
Which system(s)?
  Confocal/spinning disk
  Multiphoton
  High content (Celigo/Operetta/ImageXpress)
  TIRF
  Lightsheet
  Any others?

## Slide 81
Questions
Are you currently using microscopy or planning to?
Which system(s)?
  Confocal/spinning disk
  Multiphoton
  High content (Celigo/Operetta/ImageXpress)
  TIRF
  Lightsheet
  Any others?
Which analysis software?

## Slide 82
Questions
Are you currently using microscopy or planning to?
Which system(s)?
  Confocal/spinning disk
  Multiphoton
  High content (Celigo/Operetta/ImageXpress)
  TIRF
  Lightsheet
  Any others?
Which analysis software?
A bit / no / lots of experience?

## Slide 83
Questions
Are you currently using microscopy or planning to?
Which system(s)?
  Confocal/spinning disk
  Multiphoton
  High content (Celigo/Operetta/ImageXpress)
  TIRF
  Lightsheet
  Any others?
Which analysis software?
A bit / no / lots of experience?
Any specific aims?

## Slide 84
First (and most important lesson)
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 85
Software
Notes: Lots of software. Not much point teaching a specific one, going to go through fundamental principles.

## Slide 86
FIJI (FIJI is just ImageJ)
http://forum.imagej.net/
https://fiji.sc/

## Slide 87
FIJI (FIJI is just ImageJ)
Free
Open source
Cross platform
Flexible
Huge community
http://forum.imagej.net/
https://fiji.sc/

## Slide 88
Why computational image analysis?
Notes: Lots of data, can’t analyse manually. Inspection of data doesn’t help when comparing lots of studies.

## Slide 89
Why computational image analysis?
Quantity of data (TB’s per day)
Notes: Lots of data, can’t analyse manually. Inspection of data doesn’t help when comparing lots of studies.

## Slide 90
Why computational image analysis?
Quantity of data (TB’s per day)
Reproducibility, comparison
Notes: Lots of data, can’t analyse manually. Inspection of data doesn’t help when comparing lots of studies.

## Slide 91
Why computational image analysis?
Visual system relies heavily on context and relative changes.
Checker shadow illusion, Edward Adelson 1995.
Notes: Most importantly – eye is very easy to fool.

## Slide 92
Why computational image analysis?
Visual system relies heavily on context and relative changes.
Checker shadow illusion, Edward Adelson 1995.
Notes: Most importantly – eye is very easy to fool.

## Slide 93
Why computational image analysis?
Visual system relies heavily on context and relative changes.
Checker shadow illusion, Edward Adelson 1995.
Jastrow illusion, Joseph Jastrow (and others), 1892.
Notes: Most importantly – eye is very easy to fool.

## Slide 94
Nearly all microscopy images aren’t colour

## Slide 95
Nearly all microscopy images aren’t colour

## Slide 96
Nearly all microscopy images aren’t colour

## Slide 97
Lookup tables (LUTs)

## Slide 98
Images are arrays of numbers
78 | 64 | 71 | 57 | 43 | 44
86 | 93 | 69 | 60 | 48 | 46
75 | 64 | 57 | 59 | 55 | 62
70 | 65 | 69 | 85 | 56 | 54
54 | 68 | 88 | 63 | 46 | 43
51 | 51 | 74 | 66 | 43 | 35
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 99
More complicated images are still arrays of numbers
2D
78 | 64 | 71 | 57 | 43 | 44
86 | 93 | 69 | 60 | 48 | 46
75 | 64 | 57 | 59 | 55 | 62
70 | 65 | 69 | 85 | 56 | 54
54 | 68 | 88 | 63 | 46 | 43
51 | 51 | 74 | 66 | 43 | 35
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 100
More complicated images are still arrays of numbers
2D
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 101
More complicated images are still arrays of numbers
2D
RGB
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 102
More complicated images are still arrays of numbers
2D
3D
RGB
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 103
More complicated images are still arrays of numbers
2D
3D
RGB
Time-lapse
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 104
More complicated images are still arrays of numbers
2D
3D
RGB
Time-lapse
3D RGB
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 105
More complicated images are still arrays of numbers
2D
3D
RGB
Time-lapse
3D RGB
3D time-lapse
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 106
More complicated images are still arrays of numbers
2D
Time-lapse
3D
3D time-lapse
RGB
3D RGB
3D RGB time-lapse
Notes: Important to remember that images are just arrays of numbers, and all image processing is mathematical operations upon these numbers.

## Slide 107
Image processing vs analysis
Notes: During image analysis, lots of the work will be image processing, i.e. getting the image ready to be analysed.

## Slide 108
Image processing vs analysis
Volume
Shape
Texture
Notes: During image analysis, lots of the work will be image processing, i.e. getting the image ready to be analysed.

## Slide 109
Image processing vs analysis
Volume
Shape
Texture
Notes: During image analysis, lots of the work will be image processing, i.e. getting the image ready to be analysed.

## Slide 110
Histogram
Open any sample image
Notes: Histogram shows how many pixels are of each possible intensity,

## Slide 111
Histogram
Open any sample image
Open histogram
Notes: Histogram shows how many pixels are of each possible intensity,

## Slide 112
Thresholding
Threshold (κ)
Notes: To perform a simple threshold, pick a point on the histogram. All pixels below a point belong to one class, and all pixels above it belong to the other.

## Slide 113
Thresholding
Notes: Choosing the right value for this threshold is obviously important. Too high, and features of interest won’t be detected. Too low, and other structures in the image will be detected too.

## Slide 114
Thresholding
Notes: Choosing the right value for this threshold is obviously important. Too high, and features of interest won’t be detected. Too low, and other structures in the image will be detected too.

## Slide 115
Thresholding
Notes: Choosing the right value for this threshold is obviously important. Too high, and features of interest won’t be detected. Too low, and other structures in the image will be detected too.

## Slide 116
Thresholding – try it out
Open DAPI.tif

## Slide 117
Thresholding – try it out
Open DAPI.tif
Threshold

## Slide 118
Manual threshold - problems
DAPI.tif

## Slide 119
Manual threshold - problems
DAPI.tif
DAPI_2.tif

## Slide 120
Automatic thresholding – Equal masses
Ideal case

## Slide 121
Automatic thresholding – Equal masses
Real case
Ideal case

## Slide 122
Automatic thresholding – Otsu’s method
Minimise within class variance (σW)
Maximise between class variance (σB)
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 123
Automatic thresholding – Otsu’s method
Minimise within class variance (σW)
Maximise between class variance (σB)
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 124
Automatic thresholding – Otsu’s method
Minimise within class variance (σW)
Maximise between class variance (σB)
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 125
Unimodal thresholding – Rosin’s method
Rosin (2001) Pattern Recognition. Vol 34, No 11, p2083
Use shape of distribution to find threshold

## Slide 126
Unimodal thresholding – Rosin’s method
Rosin (2001) Pattern Recognition. Vol 34, No 11, p2083
Use shape of distribution to find threshold

## Slide 127
Try it out – Otsu’s method
Otsu (1979) IEEE Transactions on Systems, Man and Cybernetics. Vol SMC-9, No 1, p62

## Slide 128
Many, many other methods
Kapur et al. (1985) Graphical Models and Image Processing Vol 29, No 3, p273

## Slide 129
Not always that simple …
Open DAPI_3.tif
Pick a threshold
vs

## Slide 130
Background subtraction – e.g. vignetting
Sample

## Slide 131
Background subtraction – e.g. vignetting
Sample
Microscope

## Slide 132
Background subtraction – e.g. vignetting
Sample
Microscope
Image

## Slide 133
Background subtraction – e.g. vignetting

## Slide 134
Background subtraction – e.g. vignetting

## Slide 135
Background subtraction – e.g. vignetting

## Slide 136
Background subtraction – e.g. vignetting
How to calculate??

## Slide 137
Estimate background – Gaussian smoothing
Seems arbitrary, but smoothing is often a key step in image processing

## Slide 138
Estimate background – Gaussian smoothing
Seems arbitrary, but smoothing is often a key step in image processing

## Slide 139
Estimate background – Gaussian smoothing
Seems arbitrary, but smoothing is often a key step in image processing
Try a value of 200 pixels

## Slide 140
Estimate background – Gaussian smoothing
May need to adjust brightness

## Slide 141
Estimate background – Gaussian smoothing
May need to adjust brightness

## Slide 142
Estimate background

## Slide 143
Estimate background

## Slide 144
Now try thresholding

## Slide 145
Now try thresholding
Better, but not great

## Slide 146
Morphological operations
Processing of (usually binary) images based on shape

## Slide 147
Morphological operations
Try on the previous example
Thresholded

## Slide 148
Morphological operations
Try on the previous example
Eroded
Thresholded

## Slide 149
Morphological operations
Try on the previous example
Eroded
Thresholded
Dilated and closed

## Slide 150
Watershed – separate objects
From the previous example
Notes: Basic implementation in ImageJ – but often requires a lot of tweaking if you don’t have two perfectly circular objects.

## Slide 151
Watershed – separate objects
From the previous example
Notes: Basic implementation in ImageJ – but often requires a lot of tweaking if you don’t have two perfectly circular objects.

## Slide 152
Watershed – separate objects
From the previous example
Notes: Basic implementation in ImageJ – but often requires a lot of tweaking if you don’t have two perfectly circular objects.

## Slide 153
Watershed

## Slide 154
Watershed

## Slide 155
Watershed

## Slide 156
Watershed
Distance transform
Negative intensity profile

## Slide 157
Watershed
Distance transform
Negative intensity profile

## Slide 158
Watershed
Distance transform
Negative intensity profile

## Slide 159
Watershed
Distance transform
Negative intensity profile

## Slide 160
Watershed
Distance transform
Negative intensity profile

## Slide 161
Watershed
Distance transform
Negative intensity profile
Watershed

## Slide 162
Filters - Gaussian
Large kernel (200 pix)
Correct inhomogeneous illumination

## Slide 163
Filters - Gaussian
Smooth intensity variations for thresholding
Small kernel (8 pix)

## Slide 164
Filters - Gaussian
Open foci.tif & try thresholding
Apply Gaussian smoothing (use preview) & try again

## Slide 165
Filters - Gaussian
Open foci.tif & try thresholding
Apply Gaussian smoothing (use preview) & try again
vs

## Slide 166
Filters - Gradient
Edge detection

## Slide 167
Filters - Gradient
Edge detection
Approximate derivative:
  The Sobel operator

## Slide 168
Filters - Gradient
Edge detection
Approximate derivative:
  The Sobel operator
*

## Slide 169
Filters - Gradient
Edge detection
Approximate derivative:
  The Sobel operator

## Slide 170
Filters - Gradient

## Slide 171
Filters - Gradient

## Slide 172
Filters - Gradient
Combine

## Slide 173
Filters - Gradient
Combine

## Slide 174
Boolean image mathematics

## Slide 175
Boolean image mathematics
AND

## Slide 176
Boolean image mathematics
AND
OR

## Slide 177
Boolean image mathematics
AND
OR
XOR

## Slide 178
Boolean image mathematics - masking

## Slide 179
Boolean image mathematics - masking
PV.tif
PV_DAPI.tif

## Slide 180
Boolean image mathematics - masking
PV.tif
PV_DAPI.tif
PV_seg.tif

## Slide 181
Boolean image mathematics - masking
PV.tif
PV_DAPI.tif
PV_seg.tif

## Slide 182
First (and most important lesson) – again!
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 183
Deconvolution
Sample

## Slide 184
Deconvolution
Sample
PSF

## Slide 185
Deconvolution
Sample
Blurred
PSF

## Slide 186
Deconvolution
Sample
Blurred
PSF
Noise

## Slide 187
Deconvolution
Sample
Blurred
Blurred & noisy
PSF
Noise

## Slide 188
Deconvolution
Sample
Blurred
Blurred & noisy
PSF
Noise
?

## Slide 189
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy

## Slide 190
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Image
Operation

## Slide 191
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Estimate
Image
Operation

## Slide 192
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Estimate
PSF
Image
Operation

## Slide 193
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Estimate
Convolved
estimate
PSF
Image
Operation

## Slide 194
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Estimate
Compare with raw
Convolved
estimate
PSF
Raw Image
Image
Operation

## Slide 195
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Estimate
Compare with raw
Improve estimate
Convolved
estimate
PSF
Raw Image
Image
Operation

## Slide 196
Convolve with PSF
Deconvolution – how?
Lucy (1974) The Astronomical Journal. Vol 79, No 6 p745
Richardson (1972) Journal of the Optical Society of America, Vol 62, No 1, p55
Constrained iterative deconvolution
e.g. Richardson-Lucy
Raw Image
Deconvolved
Estimate
Compare with raw
Improve estimate
Convolved
estimate
PSF
Raw Image
Image
Operation

## Slide 197
Deconvolution – try it out
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
DeconvolutionLab2 (already installed)
Sage et al. (2017) Methods. Vol 115, p28

## Slide 198
Deconvolution – try it out
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
DeconvolutionLab2 (already installed)
Sage et al. (2017) Methods. Vol 115, p28

## Slide 199
Deconvolution – try it out
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
DeconvolutionLab2 (already installed)
Drag and drop
CElegans-FITC.tif
PSF-CElegans-FITC.tif
C. Elegans embryo - microtubules
Sage et al. (2017) Methods. Vol 115, p28

## Slide 200
Deconvolution – try it out
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
DeconvolutionLab2 (already installed)
Drag and drop
CElegans-FITC.tif
PSF-CElegans-FITC.tif
C. Elegans embryo - microtubules
Sage et al. (2017) Methods. Vol 115, p28

## Slide 201
Deconvolution – try it out (hopefully)
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
Deconvolution is computationally intense – may be very slow on these machines

## Slide 202
Deconvolution – try it out (hopefully)
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
Deconvolution is computationally intense – may be very slow on these machines
Try “Regularized Inverse Filter”

## Slide 203
Deconvolution – try it out (hopefully)
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
Deconvolution is computationally intense – may be very slow on these machines
Try “Regularized Inverse Filter”

## Slide 204
Deconvolution – try it out (hopefully)
http://bigwww.epfl.ch/deconvolution/deconvolutionlab2/
Deconvolution is computationally intense – may be very slow on these machines
Try “Regularized Inverse Filter”
Richardson-Lucy – start with 10 iterations - compare

## Slide 205
Deconvolution – notes

## Slide 206
Deconvolution – notes
GIGA – Garbage In, Garbage Out

## Slide 207
Deconvolution – notes
Not always necessary
GIGA – Garbage In, Garbage Out

## Slide 208
Deconvolution – notes
Not always necessary
Only an estimate of fluorophore distribution
GIGA – Garbage In, Garbage Out

## Slide 209
Deconvolution – notes
Not always necessary
Only an estimate of fluorophore distribution
100’s of algorithms and options – try them out
GIGA – Garbage In, Garbage Out

## Slide 210
Deconvolution – notes
Not always necessary
Only an estimate of fluorophore distribution
100’s of algorithms and options – try them out
Can be very slow
GIGA – Garbage In, Garbage Out

## Slide 211
Deconvolution – notes
Not always necessary
Only an estimate of fluorophore distribution
100’s of algorithms and options – try them out
Can be very slow
Requires a good quality measured PSF (estimated PSF’s can work for standard microscopes)
  Routine to measure each day on light-sheet systems (e.g. lattice)
GIGA – Garbage In, Garbage Out

## Slide 212
Machine Learning
Often intensity alone can’t be used for segmentation
Need “context”
Train the computer to “recognize” structures

## Slide 213
Machine Learning
Often intensity alone can’t be used for segmentation
Need “context”
Train the computer to “recognize” structures
Open CHO.tif

## Slide 214
Machine Learning
Try to threshold!

## Slide 215
Machine Learning – Trainable Weka Segmentation

## Slide 216
Machine Learning – Trainable Weka Segmentation

## Slide 217
Machine Learning – Trainable Weka Segmentation

## Slide 218
Machine Learning – Trainable Weka Segmentation
Lots of training data

## Slide 219
Machine Learning – Trainable Weka Segmentation
Lots of training data
Choose features carefully

## Slide 220
Machine Learning – Trainable Weka Segmentation
Lots of training data
Choose features carefully
Will be slow!

## Slide 221
Machine Learning – Trainable Weka Segmentation
Lots of training data
Choose features carefully
iLastik
Will be slow!

## Slide 222
Analysis (rather than processing)
Measure segmented objects

## Slide 223
Analysis (rather than processing)
Measure segmented objects

## Slide 224
Analysis (rather than processing)
Measure segmented objects

## Slide 225
Analysis

## Slide 226
Analysis
Measure other objects
  Draw, then measure

## Slide 227
Analysis
Measure other objects
  Draw, then measure

## Slide 228
Analysis
Multiple objects – ROI manager

## Slide 229
Analysis
Multiple objects – ROI manager

## Slide 230
Analysis
Multiple objects – ROI manager

## Slide 231
Analysis – 3D

## Slide 232
Analysis – 3D

## Slide 233
Analysis – 3D

## Slide 234
Analysis – 3D

## Slide 235
Macros - record
Automated
Quicker
Reproducible (sharing)
Less chance for bias/mistakes
Works with most ImageJ plugins
No coding required (but possible)

## Slide 236
Macros - record
Automated
Quicker
Reproducible (sharing)
Less chance for bias/mistakes
Works with most ImageJ plugins
No coding required (but possible)

## Slide 237
Macros – edit & run
Use comments (lines starting with “//”) for notes/explanations

## Slide 238
Macros – edit & run
Use comments (lines starting with “//”) for notes/explanations

## Slide 239
How to make your analysis easier – plan!

## Slide 240
How to make your analysis easier – plan!
Use the correct method
  Widefield
  Confocal
  Multiphoton
  TIRF
  Super resolution (PALM/STORM/SRRF)
  Light sheet (iSPIM/diSPIM/Lattice)
  Something else – flow cytometry, biochemistry?

## Slide 241
How to make your analysis easier – plan!
Use the correct method
  Widefield
  Confocal
  Multiphoton
  TIRF
  Super resolution (PALM/STORM/SRRF)
  Light sheet (iSPIM/diSPIM/Lattice)
  Something else – flow cytometry, biochemistry?
Choose dyes carefully (SNR!)
  mNeonGreen vs EGFP
  Alexa 488 vs FITC

## Slide 242
Resolution

## Slide 243
Resolution
Resolution depends on:
  Wavelength of light
  Refractive index of media (n)
  NA of objective
  (Width of light sheet)

## Slide 244
Resolution
Resolution depends on:
  Wavelength of light
  Refractive index of media (n)
  NA of objective
  (Width of light sheet)

## Slide 245
Resolution
Resolution depends on:
  Wavelength of light
  Refractive index of media (n)
  NA of objective
  (Width of light sheet)
Nyquist theorem
  Sampling frequency (how many pixels) should be ≤ resolution
  Modern acquisition software will do this for you.

## Slide 246
Resolution – However!

## Slide 247
Resolution – However!
What do you want to image?

## Slide 248
Resolution – However!
What do you want to image?
0.916 pix μm-1
15.4 pix μm-1

## Slide 249
Resolution – However!
What do you want to image?
0.916 pix μm-1
15.4 pix μm-1
Same information – 300 x less data
  Also maybe quicker and more gentle

## Slide 250
Resolution – 3D
If you want to analyse in 3D:
  Isotropic resolution

## Slide 251
Resolution – 3D
If you want to analyse in 3D:
  Isotropic resolution
2D

## Slide 252
Resolution – 3D
If you want to analyse in 3D:
  Isotropic resolution
2D
3D

## Slide 253
Note – 3D analysis
Analysis almost always exactly the same as 2D:
  Takes longer
  Need to view in 3D to check
  3D not necessarily supported by software package

## Slide 254
Resolution – temporal

## Slide 255
Resolution – temporal

## Slide 256
Resolution – temporal

## Slide 257
Resolution – temporal

## Slide 258
Resolution – temporal

## Slide 259
Resolution – temporal

## Slide 260
Resolution – temporal

## Slide 261
Resolution – temporal

## Slide 262
Resolution – temporal

## Slide 263
Resolution – temporal
Accurate sampling vs photobleaching & data size

## Slide 264
Signal to noise ratio (SNR)
Resolution irrelevant if you can’t detect structures of interest

## Slide 265
Signal to noise ratio (SNR)
Resolution irrelevant if you can’t detect structures of interest
High resolution
Low resolution
High SNR
Low SNR

## Slide 266
Signal to noise ratio (SNR)
Resolution irrelevant if you can’t detect structures of interest
High resolution
Low resolution
High SNR
Low SNR
Contrast often the most important aspect of a good image

## Slide 267
Analysis as a method

## Slide 268
Analysis as a method
“True” image

## Slide 269
Analysis as a method
“True” image
Observed widefield image

## Slide 270
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 271
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 272
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 273
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 274
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 275
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
STORM/PALM

## Slide 276
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
Localised fluorophores
STORM/PALM

## Slide 277
Analysis as a method
“True” image
Observed widefield image
STORM/PALMaquisition
Localised fluorophores
Reconstructed image
STORM/PALM

## Slide 278
First (and most important lesson) – again!
Test your analysis before you acquire data!
Sample
preparation
Data
Analysis
Biological information

## Slide 279
Any other courses?

## Slide 280
Any other courses?
General – more advanced

## Slide 281
Any other courses?
General – more advanced
3D

## Slide 282
Any other courses?
General – more advanced
3D
Big datasets

## Slide 283
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing

## Slide 284
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution

## Slide 285
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution

## Slide 286
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution
Tracking

## Slide 287
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution
Tracking
Writing custom scripts – MATLAB / Python etc

## Slide 288
Any other courses?
General – more advanced
3D
Big datasets
Lightsheet processing
Super resolution
Tracking
Writing custom scripts – MATLAB / Python etc
Anything else?